## Slide 1: Floating Point Numbers

## Slide 2: Exponential Notation
The representations differ in that the decimal place – the “point” -- “floats” to the left or right (with the appropriate adjustment in the exponent).
The following are equivalent
representations of 1,234
123,400.0 x 10-2
12,340.0 x 10-1
1,234.0 x 100
123.4 x 101
12.34 x 102
1.234 x 103
0.1234 x 104

## Slide 3: Parts of a Floating Point Number
-0.9876 x 10-3
Sign of mantissa
Location of decimal point
Mantissa
Exponent
Sign of exponent
Base

## Slide 4: IEEE 754 Standard for representing floating point numbers
Single precision: 32 bits, consisting of...
  Sign bit (1 bit)
  Exponent (8 bits)
  Mantissa (23 bits)
IEEE = Institute of Electrical and Electronics Engineers
Double precision: 64 bits, consisting of…
  Sign bit (1 bit)
  Exponent (11 bits)
  Mantissa (52 bits)

## Slide 5: Single Precision Format (32 bits)
Mantissa (23 bits)
Exponent (8 bits)
Sign of mantissa (1 bit)

## Slide 6: Normalization
The mantissa is normalized
Has an implied decimal place on left
Has an implied “1” on left of the decimal place
e.g.,
  Mantissa 
  Represents…
10100000000000000000000
1.1012 = 1.62510

## Slide 7: Excess Notation
To include +ve & –ve exponents, “excess” notation is used
Single precision: excess 127 (1023 for double precision)
The value of the exponent stored is larger than the actual exponent, e.g., excess 127,
  Exponent  127
  Represents…
10000111
135 – 127 = 8
+ve - positive
Notes: Excess - nadmiar

## Slide 8: Example
Single precision
0 10000010 11000000000000000000000
1.112
130 – 127 = 3
0 = positive mantissa
+1.112 x 23 = 1110.02 = 14.010
1.

## Slide 9: Hexadecimal
It is convenient and common to represent the original floating point number in hexadecimal
The preceding example…
0 10000010 11000000000000000000000
4
1
6
0
0
0
0
0

## Slide 10: Converting from Floating Point
E.g.,
what decimal value is represented by the following 32-bit floating point number?
C17B000016

## Slide 11
Step 1
  Express in binary and find S, E, and M
C17B000016 =
1 10000010 111101100000000000000002
S
E
M
1 = negative
0 = positive

## Slide 12
Step 2
  Find “real” exponent, n
  n = E – 127
  = 100000102 – 127
  = 130 – 127
  = 3

## Slide 13
Step 3
  Put S, M, and n together to form binary result
  (Don’t forget the implied “1.” on the left of the mantissa.)
-1.11110112 x 2n =
-1.11110112 x 23 =
-1111.10112
1.

## Slide 14
Step 4
  Express result in decimal
-1111.10112
-15
2-1 = 0.5
2-3 = 0.125
2-4 = 0.0625
0.6875
Answer: -15.6875

## Slide 15: Converting to Floating Point
E.g.,
Express 36.562510 as a 32-bit floating point number (in hexadecimal)

## Slide 16
Step 1
  Express original value in binary
36.562510 =
100100.10012

## Slide 17
Step 2
  Normalize
100100.10012 =
1.0010010012 x 25

## Slide 18
Step 3
  Determine S, E, and M
+1.0010010012 x 25
S = 0 (because the value is positive)
M
S
n
E = n + 127
= 5 + 127
= 132
= 100001002

## Slide 19
Step 4
  Put S, E, and M together to form 32-bit binary result
0 10000100 001001001000000000000002
S
E
M

## Slide 20
Step 5 - Express in hexadecimal
0 10000100 001001001000000000000002 =
0100 0010 0001 0010 0100 0000 0000 00002 =
4 2 1 2 4 0 0 016
Answer: 4212400016

## Slide 21
(A + B) + C ≠ A + (B + C)