## Slide 1: Logic gates
4 different names have been
used for the same type of circuits:
digital circuits,
switching circuits,
logic circuits & gates
circuit [`sə:kɪt] – obwód (el.) , układ integrated circuit - obwód scalony

## Slide 2: A logic gate is a device*)
implementing a Boolean function, i.e. it performs a logical operation on 1+ logic inputs and produces a single logic output.
*) idealized or physical
Notes: primarily 1. (originally) pierwotnie. 2. (principally, essentially) głównie, przede wszystkim.
relay - (electr) przekaźnik
Amplification (expansion, extension) rozwinięcie; (enlargement) rozszerzenie

## Slide 3: Logic gates
are primarily implemented using diodes or transistors acting as electronic switches, but can also be constructed using electromagnetic relays, fluidic logic, pneumatic logic, optics, molecules, or even mechanical elements.
Logic gates can be cascaded in the same way that Boolean functions can be composed, allowing the construction of a physical model of all of Boolean logic, and therefore, all of the algorithms and mathematics that can be described with Boolean logic
Notes: primarily 1. (originally) pierwotnie. 2. (principally, essentially) głównie, przede wszystkim.
relay - (electr)przekaźnik
Amplification (expansion, extension) rozwinięcie; (enlargement) rozszerzenie

## Slide 4: AND gate
The AND gate is an electronic circuit that gives a high output (1) only if all its inputs are high

## Slide 5: OR gate
The OR gate is an electronic circuit that gives a high output (1) if one or more of its inputs are high.
AND gate

## Slide 6: NOT gate (the Inverter)
The NOT gate is an electronic circuit that produces an inverted version of the input at its output.
It is also known as an inverter.
If the input variable is A, the inverted output is known as NOT A.

## Slide 7: Universal Gates: NAND and NOR
AND/OR/NOT gates are sufficient for building any Boolean functions:
However, other gates are also used because:
  usefulness
  economical on transistors
  self-sufficient
NAND/NOR : economical, self-sufficient
XOR : useful (e.g. parity bit generation)
the set {AND, OR, NOT} a complete set of logic
Notes:   usefulness [`ju:sfulnɪs] użyteczność

## Slide 8: NAND gate
This is a NOT-AND gate which is equal to an AND gate followed by a NOT gate.
The outputs of all NAND gates are high if any of the inputs are low

## Slide 9: NAND gate
NAND gate is self-sufficient,
can build any logic circuit with it:
{NAND} is a complete set of logic
Can be used to implement AND/OR/NOT.
Implementing an inverter using NAND gate:
(xx)' = x' (idempotency)

## Slide 10: Implementing AND using NAND gates
((xy)'(xy)')'= ((xy)') ' idempotency
= (xy) involution
idempotency – identical, identical nature, identical twins
Notes: idempotency – identical, identical nature, identical twins

## Slide 11: Implementing OR using NAND gates
((xx)'(yy)')'= (x'y')' idempotency
= x''+y'' DeMorgan
= x+y involution

## Slide 12: NOR gate
This is a NOT-OR gate which is equal to an OR gate followed by a NOT gate.
The outputs of all NOR gates are low if any of the inputs are high.

## Slide 13: NOR gate
NOR gate is self-sufficient.
Therefore, {NOR} is a complete set of logic
Can be used to implement AND/OR/NOT.
Implementing an inverter using NOR gate:
(x+x)' = x' (idempotency)

## Slide 14: Implementing AND & OR using NOR gates

## Slide 15: XOR gate (=EOR gate, or EXOR gate)
XOR(A,B) = AB’+A’B (as logical expression)
XOR is one or the other but not both.

## Slide 16: (E)XNOR gate (logical equality)
The 'Exclusive-NOR' gate circuit does the opposite to the EOR gate. It will give a low output if either, but not both, of its two inputs are high
XNOR gate constructed
using only NAND gates:

## Slide 17
All 2-input Gates |  |  |  |  |  |  | 
A | B | AND | NAND | OR | NOR | EX-OR XOR | EX-NOR
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
 |  | AB | (AB)’ | A+B | (A+B)’ | A B | (AB)’
 |  |  | AB |  | A+B | Note that EX-OR and EX-NOR gates can have only 2 inputs. | 

## Slide 18: Logic Diagrams and Expressions
Boolean equations, truth tables & logic diagrams describe the same function!
X
Y
F
Z
Logic Diagram
Logic Equation
Z
Y
X
F
+
=
Truth Table
1
1 1 1
1
1 1 0
1
1 0 1
1
1 0 0
0
0 1 1
0
0 1 0
1
0 0 1
0
0 0 0
F = X + Y Z
X Y Z
Notes: Truth tables are unique, but expressions and logic diagrams are not. This gives flexibility in implementing functions.

## Slide 19: Drawing Logic Circuit
When a Boolean expression is provided, we can easily draw the logic circuit. Examples:
(1) F1 = xyz’‚ (note the use of a 3-input AND gate)
Circuit [`sə:kɪt] - obwód, układ
Notes: Circuit [`sə:kɪt] - obwód, układ

## Slide 20: Drawing Logic Circuit
F2 = x + y'z
(can assume that variables and their complements are available)
(3) F3 = xy' + x'z
Notes: Circuit [`sə:kɪt] - obwód, układ
Cd:
http://www.scribd.com/doc/390129/Introduction-to-Logic-Gates

## Slide 21: Analysing Logic Circuit
When a logic circuit is provided, we can analyse the circuit to obtain the logic expression.
Example: What is the Boolean expression of F4?
F4 = (A'B'+C)' = (A+B)C'
Notes: Circuit [`sə:kɪt] - obwód, układ
Cd:
http://www.scribd.com/doc/390129/Introduction-to-Logic-Gates

## Slide 22: Truth table -> Logic Expression -> Diagram
Boolean equation,, truth table & logic diagram describe the same function!
Notes: Truth tables are unique, but expressions and logic diagrams are not. This gives flexibility in implementing functions.

## Slide 23: Substituting one type of gate for another
Making a NOT gate from a NAND or NOR gate. Reducing a NAND or NOR gate to just one input creates a NOT gate.
Any gate can be built from NAND or NOR gates
The diagrams show this for a 2-input NAND and NOR gates:

## Slide 24: NAND gate equivalents
Gate |  | Equivalent in NAND gates
NOT |  | 
AND |  | 
OR |  | 
NOR |  | 
Notes: Lab Quiz 1
https://sites.google.com/site/stephenmatthewssite/lab-quiz-1

## Slide 25: EXAMPLE 2
XOR gate constructed using only NAND gates:

## Slide 26: LOGIC GATES
Type | Distinctive shape ANSI/IEEE Std | Boolean algebra between A & B
AND |  | AB, AB
OR |  | A + B
NOT |  | A
NAND |  | AB, AB
NOR |  | A + B
XOR |  | A  B
XNOR |  | A  B, A  B
Type | Distinctive shape ANSI/IEEE Std | Boolean algebra between A & B
AND |  | 
OR |  | A + B
NOT |  | A
NAND |  | 
NOR |  | A + B
XOR |  | A  B
XNOR |  | A  B, A  B